## Slide 1: Korea Made Coronary Devices: Present and Future
Taehoon Ahn, MD, PhD, FSCAI, FACC
Gachon University Gil Medical Center
Incheon, South Korea
JCR2016

## Slide 2
Conflict of interest: Nothing to report
Disclosure

## Slide 3
Current situation of Korea made drug-eluting stents in Korea
Future of Korea made coronary products in Korea
Global and Domestic Drug-eluting stent market/development Outlook
1
3
2
Contents:

## Slide 4: Global medical equipment market outlook
 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
North/ South America | 1,263 | 1,372 | 1,394 | 1,457 | 1,546 | 1,641 | 1,753 | 1,872 | 2,000 | 2,139
Asia / Pacific | 523 | 601 | 670 | 677 | 723 | 774 | 844 | 922 | 1,011 | 1,116
Western Europe | 761 | 823 | 792 | 848 | 880 | 885 | 900 | 947 | 997 | 1056
Central and Eastern Europe | 156 | 179 | 188 | 176 | 171 | 179 | 189 | 203 | 217 | 232
Middle East / Africa | 60 | 68 | 74 | 80 | 83 | 91 | 100 | 111 | 122 | 136
Total | 2,763 | 3,043 | 3,117 | 3,238 | 3,403 | 3,571 | 3,785 | 4,054 | 4,348 | 4,678
Unit: Bill $,%
출처:BMI Espicom, Worldwide Medical Market Forecasts to 2019,2014.9
출처:한국보건산업진흥원, 2014년 의료기기산업 분석 보고서 2014

## Slide 5: Medical equipment market situation in Korea
 | Production | Export | Income | Market | Share of Income
2010 | 2,964,445 | 1,681,619 (1,454,361) | 2,619,895 (2,265,836) | 3,902,720 | 67,1
2011 | 3,366,462 | 1,853,785 (1,672,925) | 2,793,709 (2,521,148) | 4,306,387 | 64,9
2012 | 3,877,374 | 2,216,074 (1,966,557) | 2,931,014 (2,600,999) | 4,592,314 | 63,8
2013 | 4,224,169 | 2,580,862 (2,356,866) | 2,988,241 (2,728,888) | 4,631,538 | 64,5
2014 | 4,604,814 | 2,714,058 (2,576,914) | 3,084,204 (2,928,357) | 4,974,960 | 62,0
Unit: Mill \ ,%
( ):one thousand dollar
KFDA 2015.05.13

## Slide 6: Cardiovascular Devices in Korea

## Slide 7: Global DES Market
(Million dollars)

## Slide 8: DES usage trends by year in Korea (HIRA 2015)
Chart: Case No
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Qualified Health Insurance | 53966 | 64087 | 66232 | 66728 | 70026 | 72937 | 74555
A beneficiary of medical care | 4565 | 4852 | 5297 | 5236 | 5142 | 5078 | 5471
Total | 58531 | 68939 | 71529 | 71964 | 75168 | 78015 | 80026
Chart: Amount
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Qualified Health Insurance | 112050642891 | 134165304225 | 135629652266 | 135257430899 | 139996358528 | 139320436732 | 141129600450
A beneficiary of medical care | 9449907472 | 10171674237 | 10880899601 | 10613708422 | 10202684022 | 9673277097 | 10321105228
Total | 121500550363 | 144336978462 | 146510551867 | 145871139321 | 150199042550 | 148993713829 | 151450705678

## Slide 9: STENT Manufacturers in Korea
1991
2012
Global Big Com.
Korean Small Com.
Korean Big Com.
M&A
M&A
M&A
Korea cardiovascular stent research institute
DIO
M&A

## Slide 10: Drug-eluting Stent Market Outlook in Korea vs. Japan
Chart: Drug-eluting Stent Market in Korea(n=74,555)
| Global Stents | Domestic Stents
Stent Market in Korea | 0.981 | 0.02
Chart: Drug-eluting Stent Market in Japan(n=250,000)
| Global stents | Domestic stents
Stent market in Japan(n=250,000) | 0.65 | 0.35
98.1%
65%
35%
2015
2015
(Nobori, Ultimaster)
(Xience Alpine, Synergy, Resolute Integrity)

## Slide 11
Stent Platforms available in Korea
DXR | Genoss | SALVUS | Xience Prime /Alpine | Synergy | Resolute Integrity /Onyx | BioMatrix Flex
Semi-open cell | Semi-open cell | Semi-open cell | Semi-open cell | Semi-open cell | Semi-open cell | Semi-open cell
L605 CoCr alloy | L605 CoCr alloy | L605 CoCr alloy + TiO2 | L605 CoCr alloy | L605 PtCr alloy | L606 CoCr alloy | 316L Stainless steel S-stent
77㎛ | 70㎛ | 75um | 81㎛ | 81㎛ | 91㎛ | 120㎛
1.04mm | 1.0mm | 1.07mm | 1.08mm | 1.07mm | 1.0mm | 1.11mm
Company
DES
Cell Design
Stent Material
Strut Thickness
Crossing Profile
Item
Domestic DES Global DES

## Slide 12
Stent Platforms available in Korea
DXR | Genoss | SALVUS | Xience Prime /Alpine | Synergy | Resolute Integrity /Onyx | BioMatrix Flex
Degradable (PLGA) | Degradable (PLGA) + Parylene | Degradable (PLGA) | Non degradable (PVDF-HFP) | Degradable (PLGA) | Non degradable (BioLinx: (C10/C19/PVP blend) | Degradable (PLA)
Fast Re-endothelialization rate | Fast Re-endothelialization rate | Fast Re-endothelialization rate | Nomal Re-endothelialization rate | Fast Re-endothelialization rate | Nomal Re-endothelialization rate | Fast Re-endothelialization rate
Paclitaxel Cilostazol (Dual drug) | Sirolimus (Single drug) | Sirolimus (Single drug) | Everolimus (Single drug) | Everolimus (Single drug) | Zotarolimus (Single drug) | Biolimus A9 (Single drug)
Full coating | Abluminal coating | Semi-Abluminal coating | Full coating | Abluminal coating | Full coating | Abluminal coating
Company
DES
Polymer
Drug
Coating
Item
Domestic DES Global DES

## Slide 13
- Active Drug A: Paclitaxel (1.0ug/mm2)
  ► Inhibiting cell proliferation makes Lower Restenosis
- Active Drug B: Cilostazol (6.0ug/mm2)
  ► Anti platelet effect makes Lower Thrombosis
Multi-layered Coating Structure
Cilotax ---DXR (Dual eXcellent Revolution)

## Slide 14
Stent | CILOTAX | DXR
Material | L605 Co-Cr Alloy (ASTM F90) | 
Cell Design | Semi-Open Cell | 
Coating Thickness | 13㎛ | 6㎛
Elastic Recoil | < 6% | < 6%
Longitudinal Compression | 0.380 mm | 0.260 mm
Longitudinal Tensile | 1.53 mm | 0.75 mm
Radial Force | 4.03 N | 4.26 N
Flexibility | 0.52 N | 0.38 N
Delivery System | CILOTAX | DXR
Balloon Material | Nylon Blend | 
Usable Catheter Length | 135 cm | 138 cm
Distal Shaft | 2.5 mm ~ 3.0 mm: 2.7 F 3.5 mm : 2.8 F | 2.5 mm ~ 3.0 mm: 2.6 F 3.5 mm : 2.7 F
Proximal Shaft | 2.0 F | 1.9 F

## Slide 15: Landmark study of Cilotax for SAP

## Slide 16: Clinical outcome of Cilotax in AMI
 | Cilotax (n=141) | Other 2nd generation (n=162) | P
MACEs, n (%) | 7 (5.0) | 4 (2.4) | 0.087
Cardiac death & MI, n (%) | 7 (5.0) | 4 (2.4) | 0.216
Cardiac death, n (%) | 2 (1.4) | 3 (2.2) | 0.682
Nonfatal MI, n (%) | 5 (3.5) | 1 (0.6) | 0.100
TLR, n (%) | 0 (0) | 1 (0.6) | 1.000
Definite stent thrombosis, n (%) | 4* (2.8) | 1+ (0.7) | 0.371
Inclusion criteria
- AMI with ST-segment elevation (≥ 20 minutes of chest pain and at least 2 mm of ST-segment elevation in at least two contiguous leads or a new left bundle-branch block) and
- Primary PCI with stent implantation (diameter stenosis >50%, ≥2.5 mm to ≤4.0 mm, de novo lesion in native coronary artery)
Exclusion criteria
- Thrombolytic therapy
- AMI caused by in-stent thrombosis or restenosis
- Cardiogenic shock
- Follow-up loss for 1 year
* Angiographic data was not evaluated yet.

## Slide 17: Current Status of Ongoing Clinical Studies

## Slide 18
Balloon Catheter
Drug
Strut
Polymer
1
2
- Co-Cr Alloy L605
- Thickness 70-78µm
Characteristics
3
4
- Sirolimus
- 1.15ug/mm2
DES
- Low profile
- Good Flexibility, pushability
- Fast deflation
- Bioresorbable polymer
- Abluminal coating
- Coating thickness 4µm
Full coating
Abluminal coating

## Slide 19
- de novo Coronary lesion
- 20 years ≤ Age ≤ 80 years
- Stable angina, Unstable angina, Silent ischemia
- 2.5mm ≤ Vessel diameter ≤ 4.0mm
- Lesion length ≤ 40mm (overlapping 허용)
Randomization to 1 : 1 stratified by Sites
Total N=80
GenossTM
(n=40)
Promus ElementTM
(n=40)
Primary End Point : In-stent late lumen loss by QCA at 9 months
First in Man Trial
DES

## Slide 20
Late Lumen Loss (9 mo)
Genoss DES

## Slide 21: 1. Clinical trials progress (126 people completed)
12M F/up completed : 98.4%
F / up schedule completed
  9M F/up : Within the first week of September 2016
  12M F/up : Within the first week of December 2016
MACE occurrence status
  A(3 case) : TLR(3)
  B(5 case) : TLR(3)/TVR(2)
구 분 | 12M F/up | MACE | Withdrawal
A(SALVUS) | 100% (N=64) | 3 | 1
B(Biomatrix Flex) | 97% (N=62) | 5 | 0
시험기기 : SALVUS / 대조기기 : BioMatrix FlexTM
Cut-off : 2016-12-10
SALVUS Study Overview
Primary endpoint ( 9M late lumen loss): Jan/2017

## Slide 22
Korea FDA approved
Clinical use since Jan 2016
Superior flexibility
- First in the world, US Patent - Novel polymer-free technology - Korea FDA approval in progress - To be released in 2017
Polymer-free NTiO2 EES
- 3D Printing technology
- PCL scaffold coated with sirolimus mixed with
PLGA and PEG
- Pre-clinical animal study
BVS
Korea cardiovascular stent research institute
CG Bio Inc.

## Slide 23: ABSORB Launching Progress in Korea
  ABSORB is reimbursed from JAN 1st, 2016 in Korea
  Until November/2016, total 1694 units of BVS implants
  More than over 80% BVS usage from Top 20 Hospitals.
7 subacute scaffold thromboses were observed by possible mechanism of underexpansion /malapposition or early D/C of DAPT. Half of them were implanted with 2.5 mm(18-28 mm) in patients with AMI(NSTEMI or STEMI)

## Slide 24
- 3D Printing technology
PCL scaffold coated with sirolimus mixed with PLGA and PEG
- Pre-clinical animal study
New Bioresorbable Drug-Eluting Mg Stent
CNUH data. Korean Patent 10-2015-0052750
CNUH data. Materials Letters 2015;141:355-8
Current Status of the development of BVS in Korea
Drug
Coated
BVS
BVS
Korea cardiovascular stent research institute

## Slide 25: Summary
In Korea, a market of medical equipment for interventional cardiology is rapidly growing over the years.
Korea made coronary DES’s developed with modern design and techniques must be verified with well designed clinical trials.
Fortunately big companies in Korea take small stent manufacturers and have potentials to invest in the near future.
Industry academic relationship is becoming more active.
Recently, BRS’s having different design from ABSORB were developed and had preclinical trials.

## Slide 26
Thanks for Your Attention!